## Slide 1
Aim
To build and analyze various resistive networks in PySpice and to compare the analysis results with the theoretical analysis results.

## Slide 2
Materials/Devices:
PySpice

## Slide 3
Work to be done:
The following circuit is a first order R-C circuit.
Assume that the capacitor is initially discharged and 10V voltage source is applied at time zero.
The circuit diagram is shown on the slide.
Simulate the circuit and plot the capacitor voltage Vc(t).

## Slide 4
1. Simulate the circuit and plot the capacitor voltage Vc(t).
Simulate the circuit and plot the capacitor voltage Vc(t).
Try these voltage sources and discuss the results:
source = circuit.VoltageSource('input', 'in', circuit.gnd, 10@u_V)
source = circuit.PieceWiseLinearVoltageSource('input', 'in', circuit.gnd, values=[(0,0), (0,10@u_V)])
source = circuit.PulseVoltageSource('input', 'in', circuit.gnd, initial_value=0@u_V, pulsed_value=10@u_V,pulse_width=100@u_ms, period=200@u_ms)

## Slide 5
a. Try these voltage sources and discuss the results:
Try these voltage sources and discuss the results:
source = circuit.VoltageSource('input', 'in', circuit.gnd, 10@u_V)
source = circuit.PieceWiseLinearVoltageSource('input', 'in', circuit.gnd, values=[(0,0), (0,10@u_V)])
source = circuit.PulseVoltageSource('input', 'in', circuit.gnd, initial_value=0@u_V, pulsed_value=10@u_V,pulse_width=100@u_ms, period=200@u_ms)

## Slide 6
b. What is Ve at t=20µs ? Find it both theoretically and by simulation.
Calculate the voltage across the capacitor at t=20µs using the RC time constant formula.
Simulate the circuit in PySpice and verify the result obtained theoretically.
Compare the results from both methods and discuss any discrepancies.

## Slide 7
c. In transient simulation, change the "step_time" parameter and observe its effect.
Explore the effect of changing the "step_time" parameter in the transient simulation.
Observe how the simulation results change with different "step_time" values.
Discuss the trade-offs between accuracy and simulation time.

## Slide 8
Final Remarks
Summarize the key concepts learned in this lab experiment.
Discuss the importance of understanding the behavior of RC circuits.
Highlight the advantages and limitations of using PySpice for circuit analysis.